How to setup Your Linksys Router to watch SMATV

Followings are instructions to setup the Linksys WRT54G (Wireless LAN router) to work with Cyberport TV Tuner to watch SMATV on a PC.

Once we have the Linksys router setup to work properly, we can access Internet via the router. However in order to watch the SMATV on a PC with the Cybverport TV Tuner via the router, following settings are required on the router.*

* We assume you have read the quick installation guide of the router and understand how to do the basic configuration of the router. If not please read it carefully.

- Launch the router webpage (please see the quick installation guide)

- Goto “Security”, uncheck the “Filter Multicast” box (see below)

3. Goto “Application & Gaming” and select “DMZ”, check “Enable” and enter the IP address of the machine you want to watch the SAMTV.

- If you have the window XP SP2 installed and the firewall enable, please do the followings:

  - Click Exception and click “Add Port”

4.2 Enter the name (e.g. smatv), the port number 5501 and select UDP as below

  - Click OK and make sure the checkbox “smatv” is checked in the exception screen (please see screen on 4.1)

By now you should be able to watch the SMATV with Cyberport TV Tuner.